## Slide 1
U-Boot
u-boot(Universal Bootloader) is an open source, multi platform bootloader..
u-boot supports interactive commands, environment variables, and booting from external media.
u-boot supports a large variety of popular CPUs and CPU families

## Slide 2
Building U-Boot
$ make <boardname>_config
$ make CROSS_COMPILE=$(CROSSTOOL-PATH)
1. u-boot.bin is the binary image. (with ELF headers striped out) used for download and Debugging
2. u-boot.map has the global addresses for symbols, etc.

## Slide 3
U-Boot Commands
Set server ip address
u-boot> setenv serverip <server ip>
Set ip address
u-boot> setenv ipaddr <I addr>
Transfer kernel image and root file system image using tftp
U-boot> tftpboot <Load address> <uImage>
For KB9202 Board
U-boot> tftpboot 21000000 uImage
U-boot> tftpboot 22000000 myfs

## Slide 4
U-Boot Commands
Mounting root file system like initial ram disk
u-boot> setenv bootargs console=ttyS0,115200n8 root=/dev/ram0 rw initrd=0x22000000,4M
u-boot> setenv bootargs console=ttyS0,115200 root=/dev/ram0 rw initrd=0x22000000,4M rootfstype=jffs2 mem=64M
Mounting root filesystem with NFS
u-boot> setenv bootargs console=ttyS0,115200 root=/dev/nfs nfsroot=192.168.1.50:/media ip=192.168.1.1
Booting kernel image from RAM
u-boot> bootm <kernel image load address>